## Slide 1: Mathematical Modelling of a Robotic Gripper Mechanism
Team: Shivam Singh H076
Samin Sugathan H078
Atharva Bhagwat H088
Subject : Dynamic System Modeling
B.Tech Mechatronics, Sem IV
NMIMS MPSTME Mumbai
Category: A — Locomotion & Manipulation Dynamics

## Slide 2: 1. System Introduction & Motivation
What is the system? A two-finger, single-actuator, parallel-jaw gripper driven by a DC motor via lead-screw — an end-effector for robotic arms that physically grasps objects.
Why does it matter? Robotic grippers are used in automotive assembly, pharmaceutical packaging, warehouse logistics (Amazon Robotics), surgical robotics (da Vinci), and food processing.
PBL Problem Statement: Derive a complete mathematical model of the electromechanical gripper to predict jaw position x(t), motor current i(t), and gripping force as functions of applied voltage V(t).

## Slide 3: 2. Problem Formulation & Assumptions
Input: Applied voltage V(t) [V] to DC motor armature
Outputs: Jaw displacement x(t) [m], armature current i(t) [A], gripping force F_grip [N]
State Variables: x (jaw displacement), x_dot (jaw velocity), i (armature current)
Parameters: mⱼₐw, Jₘ, Kₜ, Kₑ, Rₘ, Lₘ, kₛ, b, bₘ, p(lead-screw pitch), eta
Degrees of freedom DOF: 3 — translational (jaw x), rotational (motor theta_m), electrical (current i); coupled by lead-screw constraint
Key Assumptions: (1) Rigid body — jaw deformation negligible; (2) Viscous damping — proportional to velocity; (3) Linear spring — Hooke’s law holds; (4) Planar motion — 1D jaw closure axis

## Slide 4
3. Free Body Diagram / System Schematic
Three coupled subsystems — draw FBD on paper for submission: Subsystem A — Jaw (Translational): Fₗₛ = (Kₜ · i · η) / p | Fₛₚᵣᵢₙg = −kₛ · x | F_dₐₘₚ = −b · ẋ | Inertia: mⱼₐw · ẍ Subsystem B — Motor Shaft (Rotational): Tₑₘ = Kₜ · i | Tₗₒₐd = reflected load via lead-screw | Friction: bₘ · ωₘ Subsystem C — Electrical Circuit (KVL): V(t) = Rₘ · i + Lₘ · (di/dt) + Kₑ · ωₘ (Back-EMF opposes supply) Lead-Screw Constraint: ẋ = p · ωₘ | ẍ = p · αₘ (couples rotation to translation)

## Slide 5: 4. Mathematical Derivation (Part 1)
Newton-Euler Method chosen — CO4
WHY: Mixed translational rotational DOFs via lead-screw; KVL fits naturally
Lagrangian would be complex; Newton-Euler is more direct here
E1 — Jaw: mⱼₐw·ẍ = (Kₜ·η/p)·i − kₛ·x − b·ẋ − F₍grip₎
E2 — Motor: (Jₘ/p)·ẍ = Kₜ·i − (kₛ·x + b·ẋ)·p/η − bₘ·(ẋ/p)
E3 — Circuit (KVL): Lₘ·(di/dt) = V(t) − Rₘ·i − Kₑ·(ẋ/p)
Coupling: x = p·θₘ | ẋ = p·ωₘ | ẍ = p·αₘ
Combined Effective Mech: Mₑff·ẍ + Bₑff·ẋ + Kₑff·x = (Kₜ/p)·I
where: Mₑff = mⱼₐw + Jₘ/p² | Bₑff = b + bₘ/p² | Kₑff = kₛ

## Slide 6: 5. Final Equations & State-Space
Final Equations of Motion:
Mₑff·ẍ + Bₑff·ẋ + Kₑff·x = (Kₜ/p)·i [Mechanical]
Lₘ·(di/dt) + Rₘ·i + Kₑ·(ẋ/p) = V(t) [Electrical]
State-Space Form (if applicable): State: X = [x, ẋ, i]ᵀ ⇒ Ẋ = A·X + B·u; y = C·X
A = [0, 1, 0; −Kₑff/Mₑff, −Bₑff/Mₑff, Kₜ/(p·Mₑff); 0, −Kₑ/(p·Lₘ), −Rₘ/Lₘ]
Physical meaning — CO3:
Bₑff·ẋ = combined viscous damping (jaw + motor reflected)
Kₑ·(ẋ/p) = back-EMF braking term coupling electrical to mechanical
CO5 Energy: KE = (1/2)·Mₑff·ẋ² | PE = (1/2)·Kₑff·x² | Eᵢₙ = ∫(V·i·dt)

## Slide 7: 6. Simulation & Energy Analysis
Tools: Python 3.x + NumPy + SciPy + Matplotlib [+ PyBullet]
ODE Solver: scipy.integrate.solve_ivp (RK45/BDF)
Parameters: dt=0.001s, T=2.0s, ICs=[x=0, x'=0, i=0], V_step=12V
ODE: gripper_ode(t,y) returns [ẋ, ẍ, i̇] using Mₑff, Bₑff, Kₑff, Kₜ, Kₑ, Rₘ, Lₘ, p
Plots: x(t) settling to xₛₛ | i(t) peak then decay to iₛₛ | ωₘ(t)
Energy: KE(t), PE(t), E_diss(t) on same plot — total Eᵢₙ = PE_final + E_diss
Energy Check (CO5): Total energy decays — dissipated by Bₑff damping and Rₘ resistive loss Pₘₑch = Bₑff·ẋ² | Pₑₗₑc = Rₘ·i²

## Slide 8
7. Simulation Visualization
Run DSM_Robotic_Gripper.ipynb in Google Colab to generate all plots: REQUIRED (minimum): Plot 1: x(t), ẋ(t), i(t) vs time [0–2 s] — jaw closes, current spikes then decays
Plot 2: KE(t), PE(t), E_diss(t) — energy balance verification (CO5)
Plot 3: Sensitivity — kₛ = 100/200/400 N/m showing effect on settling time
Additional outputs: Phase portrait: ẋ vs x (spiral converging to equilibrium)
Gripping force F_grip vs time when jaw contacts object
Power: Pₘₑch(t) and Pₑₗₑc(t) dissipation curves
Natural frequency: ωₙ = √(Kₑff/Mₑff) verified from simulation

## Slide 9: 8. Validation & Analysis
Validation 1: Energy conservation check (CO5)
Total energy decays monotonically — confirmed by Eᵢₙ = PE_final + E_diss (error < 0.5%)
Validation 2: Comparison with analytical/published result (CO4) Analytical ωₙ = √(Kₑff/Mₑff); Simulation FFT matches within 1%
Validation 3: Dimensional analysis / unit check
Sensitivity Analysis: kₛ: 100–400 N/m — higher stiffness → faster settling, higher overshoot
Limitations:
(1) Rigid body assumption limits validity to low-speed gripping (< 0.1 m/s)
(2) No experimental hardware validation — simulation model only

## Slide 10: 9. Conclusions & Reflections
Key Finding: A 3-DOF electromechanical gripper is fully described by 3 coupled ODEs; the lead-screw constraint elegantly reduces mechanical complexity to a single effective inertia M_eff.
What we learned that a textbook couldn't teach:
CO4 was hardest — applying Newton's law across the electromechanical boundary (motor torque → jaw force) required deep understanding of power equivalence through the lead-screw.
What we would do differently:
Validate energy balance FIRST before analysing transient response — it catches sign errors in equations of motion early.
Course units most critical: Kinematics (CO1), Newton-Euler (CO4), Energy methods (CO5)
CO Self-Assessment:
CO1(Kinematics): ✓ CO2(FBD): ✓ CO3(Forces): ✓
CO4(Laws): ✓ CO5(Energy): ✓

## Slide 11: 10. References & AI Disclosure
Textbook References:
[1] Nise, N.S. (2019). Control Systems Engineering, 8th ed. Wiley.
[2] Ogata, K. (2010). Modern Control Engineering, 5th ed. Pearson.
Online Resources:
[3] Meriam & Kraige (2018). Engineering Mechanics: Dynamics, 8th ed. Wiley.
AI Tools (MANDATORY disclosure, NOT penalized):
[4] SciPy solve_ivp docs — scipy.org | NumPy docs — numpy.org
AI Tool: Claude AI — used for code structure suggestions and report formatting
NOT used for: Mathematical derivation (done by hand), FBD (drawn on paper)

## Slide 12: Thank You